## Slide 1
ST3-0
Hybrid DVR (mixed analog and IP camera channels).
ACTi Products
Introduction

## Slide 2
Contents
Value Position & Unique Selling Points
Product Offering
Solutions
Solutions: Recommended Camera Options
Vertical Markets & Applications
Where to Buy
Support and Services

## Slide 3
Value Position & Unique Selling Points
Core Value:
6-24 channel Hybrid DVR products to combine with HD analog cameras or IP cameras for the price driven projects.
Unique Selling Points:
Hybrid design – supports both analog and IP cameras
Remote access from anywhere over the IP network
Supporting all the 4 popular formats - TVI/AHD/CVI/CVBS (most known Hybrid DVR brands only support up to 3 of them)
Plug & Play
NDAA Compliant

## Slide 4
Product Offering
Matrix View

## Slide 5
Product Offering
Model | YVR-120 | YVR-121 | YVR-122
Photo |  |  | 
Type | Standalone Hybrid DVR | Standalone Hybrid DVR | Standalone Hybrid DVR
Max Analog Channels | 4 | 8 | 16
Maximum IP Channels | 2 | 4 | 8
Total Channels | 6 | 12 | 24
Storage Bays | 1 | 1 | 1
Analog Video Formats | TVI/AHD/CVI/CVBS | TVI/AHD/CVI/CVBS | TVI/AHD/CVI/CVBS
Maximum fps vs Resolution | (TVI/AHD/CVI) 5MP@20fps 4MP@30fps 2MP@30fps 1MP@60fps (CVBS) | (TVI/AHD) 5MP@12fps 4MP@15fps 2MP@30fps 1MP@30fps (CVI) 2MP@30fps 1MP@30fps (CVBS) | (TVI/AHD) 5MP@12fps 4MP@15fps 2MP@30fps 1MP@30fps (CVI) 2MP@30fps 1MP@30fps (CVBS)
NDAA | Yes | Yes | Yes

## Slide 6
Analog Camera
(Yxx Series)
Ethernet Cable
Hybrid DVR
(YVR-series)
Coaxial Cable
(with BNC connectors)
IP Camera
(ONVIF)
Solutions
Hybrid DVR (YVR-xxx) series can connect to the analog and IP cameras. The coaxial cable is used for analog connections. The IP cameras connect using the Ethernet cable using ONVIF protocol.

## Slide 7
Model | Y31 | Y32 | Y71 | Y72
Photo |  |  |  | 
Type | Analog Mini Bullet | Analog Mini Bullet | Analog Dome | Analog Dome
Resolution | 2MP | 5MP | 2MP | 5MP
Lens | f2.8mm | f2.8mm | f2.8mm | f2.8mm
Hor Viewing Angle | 90.5° | 102.2° | 90.5° | 102.2°
Analog Video Output | 1 x BNC connector, supports TVI/AHD/CVI/CVBS | 1 x BNC connector, supports TVI/AHD/CVI/CVBS | 1 x BNC connector, supports TVI/AHD/CVI/CVBS | 1 x BNC connector, supports TVI/AHD/CVI/CVBS
Maximum fps vs Resolution | (TVI/AHD/CVI) 30 fps at 1920 x 1080 (CVBS) NTSC, PAL | (TVI/AHD) 20 fps at 2592 x 1944 (CVI) 25 fps at 2880 x 1620 (CVBS) NTSC, PAL | (TVI/AHD/CVI) 30 fps at 1920 x 1080 (CVBS) NTSC, PAL | (TVI/AHD) 20 fps at 2592 x 1944 (CVI) 25 fps at 2880 x 1620 (CVBS) NTSC, PAL
Weatherproof | IP67 | IP67 | IP67 | IP67
NDAA | Yes | Yes | Yes | Yes
Solutions: Recommended Camera Options

## Slide 8
Vertical Markets & Applications
Residential
- Vandalism & theft prevention
- Safety of the residents
- Incidents investigation
Healthcare
- Property protection
- Patients monitoring
Education (schools)
- Property protection
- Students protection
- Violence and Bullying prevention
Retail
- Property protection
- Theft prevention
- Business monitoring

## Slide 9
Where to Buy
Via Authorized Resellers
https://www.acti.com/Corporate/WhereToBuy
From ACTi Corporation Directly
E-Mail: sales@acti.com
Tel (US): +1-866-410-2284 (Toll Free)
Tel (Non-US): +886-2-2656-2588

## Slide 10
Support & Services
Technical Support
- Online Customer Helpdesk - https://www.acti.com/chd
- Phone support
US: +1-866-410-2284 (Toll Free)
Other Regions: +886-2-2656-5200
RMA Services
- Warranty
- Repair services
Training
- Self-learning